## Slide 1: Design Review
Austin Keener
Joseph Spall
Joshua Oldenburg
Juan Elizondo-Villasis
Varun Madabushi

## Slide 2: Firmware Status

## Slide 3: Electrical Status
Boards were internally design reviewed
Ordered most electrical elements
  Rigid PCB from JLCPCB
  Flex PCB from PCBWay
  Components from Digi-Key
  Received everything this week

## Slide 4: Mechanical Status
Node mechanical design is complete
Utilize threaded inserts for flexible mounting configurations
Started test 3D print

## Slide 5: Mechanical Design

## Slide 6: Software Status
Microcontroller sends PC sensor ID and values
  Extendable to multiple devices
Can organize multiple sensors for viewing
Can record and save sensor values for later processing
  Stored in JSON format

## Slide 7: Bill of Materials
Ordered:
  36 flexible PCBs
  30 rigid PCBs
  Enough components for 20 sensors
Final cost of production per sensor at our prototype volume:
  $35.79
Component | Cost per Sensor
Flexible PCB | $3.02
STM32 MCU | $2.66
Rigid PCB | $1.88
Table 1. Highest cost components

## Slide 8: Next Steps: MECHANICAL
Check fit with PCB to verify tolerances
Mass production of enclosures
Node assembly
Design and make demo platform

## Slide 9: Next Steps: Electrical
Subsystem assembly and testing in this order:
  Power system
  Grid sensing system
  Communication system
Full system assembly of all sensing boards to allow testing of firmware and software

## Slide 10: Next Steps: Firmware
Test firmware on real devices
Design and implement calibration
Implement DSP algorithms (if needed)
Finalize Mbed network controller firmware

## Slide 11: Next Steps: Software
Test desktop software with functional hardware
Utilize protobuf for serialization of objects
Run multiple sensors on a bus

## Slide 12: Open Questions: Accuracy
Activations on the prototype sensor did not correlate exactly with the location of force applied
Solutions:
  Improved manufacturing and assembly
  Data recording software
    Calibration
    Real-time DSP development

## Slide 13: Open Questions: Visualization
Sensor hardware supports multiple configurations
  Visualization software must reflect this
User-defined XML file to define preferred visualization

## Slide 14: Questions?