## Slide 1: Tactio Project Proposal By team Touché
Austin Keener
Joseph Spall
Joshua Oldenburg
Juan Elizondo-Villasis
Varun Madabushi

## Slide 2: Introduction
Humans rely heavily on their tactile senses to understand the weight, shape, and texture of the objects they hold
Robots require tactile sensors to measure contact forces with objects they interact with
  Tactile sensing can enable robots to more effectively grasp and interact with objects in the real world
Notes: image source: https://66.media.tumblr.com/36827f760bb92ab2f2fac3225450c3bf/tumblr_muoh2oO6nr1qhejy8o1_640.jpg

## Slide 3: Problems with Existing Solutions
STAG | Optical Sensors (GelSight) | SparkfunX Finger Sensor
Many Wires Complex manufacturing method Market availability | High Cost Small sensing area Market availability | Small sensing area Cannot locate contact force
Notes: The existing products do not serve

## Slide 4: Target Audience
Our goal is to develop a platform for rapid development and prototyping of tactile sensing solutions
Three target communities can benefit
  Researchers
  Students
  Hobbyists
Notes: https://www.therobotreport.com/

## Slide 5: Design Goals
Chainable modular sensor units
  Simplifies design and wiring for users
Flexible mounting configurations
  Can be easily retrofitted onto existing robots
Easy third-party integration
  Compatible with popular ecosystems for electronics prototyping

## Slide 6: Design Concept

## Slide 7: Sensing Solution
Flex PCB allows film to deform
Piezoresistive film (Velostat) changes resistance with strain
Row-column pattern allows reading in 16 different points

## Slide 8: Design Alternatives - Materials
EX-STATIC
  Thin, inexpensive, and flexible conductive fabric
  Good force localization
  Poor magnitude response due to high conductivity
  Not compatible with stacked design due to very low resistance with no added strain
  Easy to short between fabric fibers

## Slide 9: Rigid PCB Circuits
Velostat film
= R11
MOSFET switches each column on to create this circuit with each row

## Slide 10: Design Alternatives - Sensing
Capacitive- Based on separation distance of two conductive elements
  Good noise immunity
  Relatively expensive
  Only works with certain materials

## Slide 11: Microcontroller Selection
STM32F042 selected based on required peripherals (CAN and ADC), memory, cost, and pin count
STM32F042 Features
Notes: Images taken from https://www.st.com/resource/en/datasheet/stm32f042k6.pdf
https://www.st.com/en/microcontrollers-microprocessors/stm32f042k6.html#overview

## Slide 12: Firmware Solution
Microcontroller running C++ code for measurement and communication
Planning to use Mbed OS 2, with STM32Cube as a fallback
Notes: Logos from https://os.mbed.com/ and https://www.st.com/content/st_com/en/stm32cube-ecosystem.html
Image from https://www.st.com/content/st_com/en/products/evaluation-tools/product-evaluation-tools/mcu-mpu-eval-tools/stm32-mcu-mpu-eval-tools/stm32-nucleo-boards/nucleo-f042k6.html#overview

## Slide 13: Communications
Utilizes CAN 2.0, a multi-master 2-wire serial bus
Up to 255 individually addressed nodes with automatic or user-controlled addressing
Network controller manages network and polls sensors

## Slide 14: Design Alternatives - Communications
Daisy-Chained UART
UART2
UART
UART1
UART1
UART2
Controller
Advantages | Concerns
Automatic position-based node addressing | Requires custom peripheral implementation in firmware
No transceiver required | Requires timing coordination
Node 1
Node 2
Node 3

## Slide 15: Software Solution
We will provide code to run on an Mbed development board to act as a CAN to USB bridge
Desktop library to interact with and visualize the sensor
Notes: Image source: https://www.st.com/content/st_com/en/products/evaluation-tools/product-evaluation-tools/mcu-mpu-eval-tools/stm32-mcu-mpu-eval-tools/stm32-nucleo-boards/nucleo-f042k6.html#overview

## Slide 16: Analysis Flow
Due to packet size, single sensor readings are split into multiple frames
Polling
Allow sensors to stabilize
Lower RAM requirements of host for reconstruction

## Slide 17: Current Status - Electrical / Materials
Prototyped sensor
  2x flexible plastic sheet with 4 copper tape rows
  Velostat in the middle
  Stack taped together at 90 deg angle
  Modeling of Velostat for ADC range

## Slide 18: Current Status - Electrical
Flex PCB
  Designed in Autodesk EAGLE
  Perimeter tabs for soldered mounting
  Rows for connection to rigid PCB
  Will be ordered when rigid is finished

## Slide 19: Current Status - Electrical
Rigid PCB
  Designed in Autodesk EAGLE
  Schematic nearing completion
  Major components
    STM32F0 MCU
    Communication
    Power
    Safety
    Driving Circuits

## Slide 20: Current Status - Electrical / Firmware
Bread-boarded circuit mimicking rigid PCB + flex PCB design
  Wrote firmware to test...
    Reading Velostat with ADCs
    Driving rows with PFETs
    Printing to screen
STM32 MCU
Driving PFETs

## Slide 21: Current Status - Communications
CAN bus testing with breadboard prototype using MCP2562 transceiver
Logic analyzer capture of CAN packet

## Slide 22: Current Status – Software
Visualization using PyQT
Parses messages from network controller
Shows sensor force location and relative magnitude

## Slide 23: Possible Problems / Issues
Issues | Severity
Flex PCB manufacturing | ❗❗❗
General PCB turnaround | ❗❗❗
Modeling Velostat force-resistance | ❗❗
Tight time-line | ❗❗
Mbed OS compatibility issue | ❗

## Slide 24: Questions?